## Slide 1: Ray Tracing

## Slide 2: 3D Rendering
The color of each pixel on the view plane
  Depends on the radiance emanating from visible surfaces
  Simplest method is ray tracing

## Slide 3: Ray Casting & Tracing
Independent lighting calculation for every pixel

## Slide 4: Ray Casting & Tracing
For each sample
  Construct ray from eye position through view plane
  Find the first surface intersected by ray through pixel
  Compute color sample based on surface radiance

## Slide 5: Ray Casting & Tracing
For each sample
  Construct ray from eye position through view plane

## Slide 6: Ray Casting
Just find the surface intersection point
  Ray from eye to the screen pixel
  No reflection or refraction
    Direct illumination
Visible surface detection
  Shadow calculation
    Ray casting from the light source position

## Slide 7: Ray Casting
Trace primary rays from camera
  Direct illumination from unblocked lights only

## Slide 8: Ray Tracing
Recursive ray casting
Inter-object light reflection effects
  Global (mutual) illumination
  For global reflection and transmission
Highly realistic quality vs. computation time
Process overview
  Bounce (reflect) or refract the ray
  Collecting its intensity
    At each reflection/refraction point

## Slide 9: Ray Tracing
Global illumination
  Shadow
  Transmission / refraction
  Inter-object reflection
Highly realistic vs. computation time
Transparency
Reflectance
Shadow

## Slide 10: Basic Ray Tracing Algorithm
For each pixel ray
  Primary ray
    Test each surface if it is intersected
  Intersected : secondary ray
    Reflection ray
    Transmission ray : transparent objects

## Slide 11: Basic Ray Tracing Algorithm
For each pixel ray
  Primary ray
    Test each surface if it is intersected
  Intersected : secondary ray
    Reflection ray
    Transmission ray : transparent objects

## Slide 12: Ray Tracing Tree
Ray tracing tree represents illumination computation
  One branch  reflection
  The other branch  transmission
  Terminated  reach the preset maximum or strike a light source
Scene
Ray Tree

## Slide 13: Ray Tracing Tree
Pixel intensity
  Sum of intensities at root node
  Start at terminal node
  If no surfaces are intersected, the intensity of background
Scene
Ray Tree
Iback
Iback
Iback
Ipixel

## Slide 14: Transparency (1/2)
Trace secondary ray in direction of refraction
Radiance for
refraction ray

## Slide 15: Transparency (2/2)
Transparency means the fraction transmitted
  KT = 1 if object is translucent
  KT = 0 if object is opaque
  0 < KT < 1 if object is semi-translucent
Transparency
Coefficient

## Slide 16: Mirror Reflection
Trace secondary ray in direction of mirror reflection
Radiance
for mirror
reflection ray

## Slide 17: Refractive Transparency (1/2)
For thin surfaces, can ignore change in direction
  Assume light travels straight through surface

## Slide 18: Refractive Transparency (2/2)
For solid objects, apply Snell’s law:
  hr sin Qr = hi sin Qi

## Slide 19: Implementation : Pseudocode
Image RayCast(Camera camera, Scene scene, int width, int height)
{
Image image = new Image(width, height);
for (int i = 0; i < width; i++) {
for (int j = 0; j < height; j++) {
Ray ray = ConstructRayThroughPixel(camera, i, j);
Intersection hit = FindIntersection(ray, scene);
image[i][j] = GetColor(hit);
}
}
return image;
}

## Slide 20: Implementation : Ray Construction
For each sample
  Construct ray through a pixel

## Slide 21: Implementation : Miscellaneous Issues
Intersections with geometric primitives
  Sphere
  Triangle
  Groups of primitives (scene)
Acceleration techniques
  Adaptive depth control
  Bounding volume hierarchies
  First-hit speedup
  Spatial partitions
    Uniform grids / octrees / BSP trees

## Slide 22: Implementation : Ray-Sphere Intersection (1/2)
Ray : P = P0 + tV
Sphere : |P - C|2 - r2 = 0

## Slide 23: Implementation : Ray-Sphere Intersection (2/2)
Ray : P = P0 + tV, sphere : |P - C|2 - r2 = 0
  |P0 + tV - C|2 - r2 = 0
    Substituting for P
Solve quadratic equation
  at2 + bt + c = 0, where
    a = |V|2 = 1 // if ray direction is normalized
    b = 2 V • (P0 - C)
    c = |P0 - C|2 – r2
P = P0 + tV

## Slide 24: Implementation : Ray-Triangle Intersection
1. Intersect ray with plane
2. Check if point is inside triangle

## Slide 25: Implementation : Ray-Plane Intersection
Ray : P = P0 + tV
Plane : P • N + d = 0
(P0 + tV) • N + d = 0
  Substituting for P
Solution
  t = -(P0 • N + d) / (V • N)
  P = P0 + tV

## Slide 26: Implementation : Ray-Triangle Intersection Revisited
Check if point inside triangle parametrically
  Compute α, β :
    P = α (T2-T1) + β (T3-T1) + T1
  Check if point inside triangle
    0 ≤ α ≤ 1 and 0 ≤ β ≤ 1
    α + β ≤ 1

## Slide 27: Implementation : Other Ray-Primitive Intersections
Cone, cylinder, ellipsoid
  Similar to sphere
Box
  Intersect 3 front-facing planes, return closest
Convex polygon
  Same as triangle (check point-in-polygon algebraically)
Concave polygon
  Same plane intersection
  More complex point-in-polygon test

## Slide 28: Implementation : Ray-Scene Intersection
Find intersection with the front-most primitive

## Slide 29: Implementation : Adaptive Depth Control
Stop generating reflected/transmitted rays
  When the computed intensity becomes less than a certain threshold
Always set a certain maximum depth
  If not, infinite number of rays would be generated
  Not always necessary to go to the maximum depth
    If the surfaces are not highly reflective

## Slide 30: Implementation : Bounding Volume Hierarchies (1/3)
Build hierarchy of bounding volumes
  Bounding volume of interior node contains all the children

## Slide 31: Implementation : Bounding Volume Hierarchies (2/3)
Bounding volumes
  Check for intersection with simple shape first
    If the ray doesn’t intersect bounding volume
      Never intersect its contents
Still needs to check for intersections with the shape

## Slide 32: Implementation : Bounding Volume Hierarchies (3/3)
Use hierarchy to accelerate ray intersections
  Intersection-test of node contents
    Only if the bounding volume is hit

## Slide 33: Implementation : Spatial Partitions (1/3)
Construct uniform grid over scene
  Index primitives according to overlaps with grid cells

## Slide 34: Implementation : Spatial Partitions (2/3)
Trace rays through grid cells
  Fast
  Incremental
Only check primitives in intersected grid cells

## Slide 35: Implementation : Spatial Partitions (3/3)
Implementation issue
  How choose suitable grid resolution?
Too little benefit if grid is too coarse.
Too much cost if grid is too fine

## Slide 36: Implementation : Octree
Called as quadtree in 2D
  Construct adaptive grid over scene
    Recursively subdivide box-shaped cells into 8 octants
    Index primitives by overlaps with cells
Generally fewer cells than the uniform grid

## Slide 37: Implementation : Binary Space Partition (BSP) (1/2)
Recursive partition space by planes

## Slide 38: Implementation : Binary Space Partition (BSP) (2/2)
Simple recursive algorithms

## Slide 39: Summary
Ray casting
Ray tracing
  Recursive ray casting
  Inter-object reflection (global illumination)
  Highly realistic quality vs. computation time

## Slide 40: Samples